## Slide 1: The Science DMZ: A Network Design Pattern for Data-Intensive Science
Jason Zurawski – zurawski@es.net
Science Engagement Engineer, ESnet
Lawrence Berkeley National Laboratory
KINBER Webinar
March 4th 2015

## Slide 2: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2015, Energy Sciences Network

## Slide 3: ESnet at a Glance
High-speed national network, optimized for DOE science missions:
  connecting 40 labs, plants and facilities with >100 networks (national and international)
  $32.6M in FY14, 42FTE
  older than commercial Internet, growing twice as fast
$62M ARRA in 2009/2010 grant for 100G upgrade:
  transition to new era of optical networking
  world’s first 100G network at continental scale
Culture of urgency:
  4 awards in past 3 years
  R&D100 Award in FY13
  “5 out of 5” for customer satisfaction in last review
  Dedicated staff to support the mission of science
© 2015, Energy Sciences Network

## Slide 4: Network as Infrastructure Instrument
    ESnet Vision: Scientific progress will be completely unconstrained by the physical location of instruments, people, computational resources, or data.
© 2015, Energy Sciences Network
Notes: Summing up ESnet’s vision in one slide, one phrase…
Physical location of instruments, people, computational resources, data. It just should not matter.
[KSTAR, SNS, ATLAS, EMSL, CRT/NERSC, STAR Detector at RHIC [BNL, NP-funded]]

## Slide 5: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2015, Energy Sciences Network

## Slide 6: Motivation
Science & Researcher are everywhere
  Size of school/endowment does not matter – there is a researcher at your facility right now that is attempting to use the network for a research activity
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors (timelines for analysis, remote users)
  Data movement and analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult (the “Wizard Gap”)
© 2015, Energy Sciences Network
Notes: Human factors – attention span, ability to manage complexity – these are constant
There is a huge amount of promise in data-intensive science. Effective use of networks can help realize those benefits.
The Science DMZ model helps address the difficulties scientists often experience with using networks.

## Slide 7: Traditional “Big Science”
© 2015, Energy Sciences Network

## Slide 8: Big Science Now Comes in Small Packages …
…and is happening on your campus. Guaranteed.
© 2015, Energy Sciences Network

## Slide 9: Understanding Data Trends
© 2015, Energy Sciences Network
Notes: Requirements workshops for all six program offices within the DOE office of Science

## Slide 10: Data Mobility in a Given Time Interval (Theoretical)
These tables available:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/
© 2015, Energy Sciences Network
Notes: This succinctly describes what the end to end data path must achieve – network, hosts, storage, application
Green: <= 100Mbps Throughput (almost all domestic locations can do this) – less than Fast Ethernet!
Black: 100Mbps to 10Gbps Throughput (most major research institutions can do this, if its running clean)
Blue 10Gbps to 100Gbps Throughput (emerging at major locations)
Orange > 100Gbps Throughput (future for many)
Note: 1TB/hour and 100TB/week fit easily within 10G of throughput

## Slide 11: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
What is important? Ordered list:
  Correctness
  Consistency
  Performance
© 2015, Energy Sciences Network
Notes: Networks are key. However, the user interface runs on systems at the edges.
The ordered list of important items is derived from the users of the network:
1) If a tool doesn’t behave correctly, the tool is broken – get another tool
2) If the tool doesn’t behave consistently, I can’t organize my life
3) Among the tools that behave correctly and consistently, choose the tool with the required performance that is easiest to use

## Slide 12: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
    We can address the first, science hasn’t fixed the 2nd (yet)
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
© 2015, Energy Sciences Network
Notes: The application sees the network as a socket.
The socket interface does not provide path diagnostics or other troubleshooting information.
TCP behaves as it does because of measures taken in the 1980s to fix the congestion collapse of the Internet
TCP makes a promise to the application – TCP will get the data to the other end, or TCP will return an error. TCP makes no promises about performance.

## Slide 13: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
© 2015, Energy Sciences Network
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 14: Lets Talk Performance …
"In any large system, there is always something broken.”
Jon Postel
Modern networks are occasionally designed to be one-size-fits-most
  e.g. if you have ever heard the phrase “converged network”, the design is to facilitate CIA (Confidentiality, Integrity, Availability)
  This is not bad for protecting the HVAC system from hackers.
Causes of friction/packet loss:
  Small buffers on the network gear and hosts
  Incorrect application choice
  Packet disruption caused by overzealous security
  Congestion from herds of mice
It all starts with knowing your users, and knowing your network
© 2015, Energy Sciences Network

## Slide 15: Putting A Solution Together
Effective support for TCP-based data transfer
  Design for correct, consistent, high-performance operation
  Design for ease of troubleshooting
Easy adoption (for all stakeholders) is critical
  Large laboratories and universities have extensive IT deployments
  Small universities/facilities have overworked/understaffed IT departments
© 2015, Energy Sciences Network
  Drastic change is prohibitively difficult
Cybersecurity – defensible without compromising performance
Borrow ideas from traditional network security
  Traditional DMZ
    Separate enclave at network perimeter (“Demilitarized Zone”)
    Specific location for external-facing services
    Clean separation from internal network
  Do the same thing for science – Science DMZ
Notes: In order to accommodate TCP, we need a pragmatic engineering solution that:
Addresses the needs
Is implementable given financial, policy, and cultural constraints
Can be defended – we cannot ignore security

## Slide 16: The Science DMZ Superfecta
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase
© 2015, Energy Sciences Network
Notes: The Science DMZ design pattern is a set of composable ideas, including:
The architectural element itself – the Science DMZ enclave
Appropriate security that does not impact performance
Dedicated systems – Data Transfer Nodes
perfSONAR
The elements of the Science DMZ can be combined in a variety of ways depending on the need

## Slide 17: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2015, Energy Sciences Network

## Slide 18: Abstract Deployment
Simplest approach : add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners (use ACLs)
  Add-on to production infrastructure – lower risk
  Identify applications that are running (e.g. the DTN is not a general purpose machine – it does data transfer, and data transfer only)
Start with a single user/user case. If it works for them in a pilot, you can expand
© 2015, Energy Sciences Network

## Slide 19: Local And Wide Area Data Flows
© 2015, Energy Sciences Network
Notes: The green data path is susceptible to TCP performance problems stemming from packet loss combined with long distances
The red data path is very low latency – loss matters much less here (though too much loss will still cause problems)
Remember the throughput vs. latency graph

## Slide 20: Non-R1 Campus
This paradigm is not just for the big guys – there is a lot of value for smaller institutions with a smaller number of users
Can be constructed with existing hardware, or small additions
  Does not need to be 100G, or even 10G. Capacity doesn’t matter – we want to eliminate friction and packet loss
  The best way to do this is to isolate the important traffic from the enterprise
Can be scoped to either the expected data volume of the science, or the availability of external facing resources (e.g. if the pipe to KINBER/3ROX/MAGPI is small – you don’t want a single user monopolizing it)
Factors:
  Are you comfortable with Layer 2 Networking?
  How rich is your cable/fiber plant?
  Can you create a dedicated facility for science?
© 2015, Energy Sciences Network

## Slide 21: Non-R1 Campus
© 2015, Energy Sciences Network
Fiber Rich Environment

## Slide 22: Non-R1 Campus
© 2015, Energy Sciences Network
Layer 2 Switching

## Slide 23: Non-R1 Campus
© 2015, Energy Sciences Network
Single Facility

## Slide 24: Non-R1 Campus
Every campus will be different
  If you are not fiber rich, other choices may be needed.
  If the researchers don’t want to move to a dedicated facility, your options are also limited
  Have discussions – lay out what is possible and what is not
ROI Statements:
  Eliminate congestion where you can – the network path for the science user does not traverse the core -> better performance for her, and everyone else
  Improve the process of science – the next time they go for an NSF/DOE/NIST grant, they can say (with confidence) the network does what they need it to do
  Encourage others that are suffering in silence to seek you out. Once you have a success story, there will be others asking about it.
© 2015, Energy Sciences Network

## Slide 25: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2015, Energy Sciences Network

## Slide 26: Performance Monitoring
Everything may function perfectly when it is deployed
Eventually something is going to break
  Networks and systems are complex
  Bugs, mistakes, …
  Sometimes things just break – this is why we buy support contracts
Must be able to find and fix problems when they occur (even if they have been that way for a long time)
Must be able to find problems in other networks (your network may be fine, but someone else’s problem can impact your users)
TCP was intentionally designed to hide all transmission errors from the user:
  “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From RFC793, 1981)
© 2015, Energy Sciences Network
Notes: Remember – TCP promises reliable data delivery, not performance
In order for scientists to see high-performance correct behavior consistently, network engineers must be able to find and fix problems quickly.
Waiting around for trouble tickets is clearly the wrong approach
Not all problems are immediately obvious – many are known as “soft failures”

## Slide 27: Soft Network Failures – Hidden Problems
Hard failures are well-understood
  Link down, system crash, software crash
  Traditional network/system monitoring tools designed to quickly find hard failures
Soft failures result in degraded capability
  Connectivity exists
  Performance impacted
  Typically something in the path is functioning, but not well
Soft failures are hard to detect with traditional methods
  No obvious single event
  Sometimes no indication at all of any errors
Independent testing is the only way to reliably find soft failures
© 2015, Energy Sciences Network
Notes: If something is down hard, it’s easy to find
Soft failures are often visible only from the end systems
This is what makes perfSONAR so valuable – it behaves as an end system behaves, but it measures what the network does
Remember – we want to find the problems BEFORE the users do

## Slide 28: Sample Soft Failures
Rebooted router with full route table
Gradual failure of optical line card
Gb/s
normal performance
degrading performance
repair
one month
© 2015, Energy Sciences Network
Notes: 2 quick examples of soft failures:
The first of these was a Cisco 6509 that had over-filled its route table due to a misconfiguration, but the config had been fixed. The performance problem persisted until the router was rebooted. This could not have been found by auditing the configuration.
The second is a relatively common problem – in a big network there are a lot of pluggable optics packs, and sometimes they just go bad. Often they cause performance problems (soft failure) for a long time before they finally die (hard failure)

## Slide 29: Testing Infrastructure – perfSONAR
perfSONAR is:
  A widely-deployed test and measurement infrastructure
    ESnet, Internet2, US regional networks, international networks
    Laboratories, supercomputer centers, universities
  A suite of test and measurement tools
  A collaboration that builds and maintains the toolkit
By installing perfSONAR, a site can leverage over 1300 test servers deployed around the world
perfSONAR is ideal for finding soft failures
  Alert to existence of problems
  Fault isolation
  Verification of correct operation
Open Source, widely supported by a number of stakeholder organizations
© 2015, Energy Sciences Network
Notes: perfSONAR is the gold standard tool for performance testing, measurement, and interdomain troubleshooting in science networks

## Slide 30: Lookup Service Directory Search: http://stats.es.net/ServicesDirectory/
© 2015, Energy Sciences Network
Notes: How to find perfSONAR servers and services

## Slide 31: perfSONAR Dashboard: http://ps-dashboard.es.net
© 2015, Energy Sciences Network
Notes: Integrating regular testing into a visualization (ESnet example).
Performance data is public
The tool can trigger alerts to notify NOC staff.
This is a very valuable tool for setting expectations

## Slide 32: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2015, Energy Sciences Network

## Slide 33: Dedicated Systems – Data Transfer Node
The DTN is dedicated to data transfer
Set up specifically for high-performance data movement
  System internals (BIOS, firmware, interrupts, etc.)
  Network stack
  Storage (global filesystem, Fibrechannel, local RAID, etc.)
  High performance tools
  No extraneous software
Limitation of scope and function is powerful
  No conflicts with configuration for other tasks
  Small application set makes cybersecurity easier
© 2015, Energy Sciences Network
Notes: All aspects of the DTN must be tuned – even the BIOS matters
Limit the scope of the DTN as well – its job is data movement, its job is not to have office software on it.
Craft a specific security profile/policy around its only task.

## Slide 34: Data Transfer Tool Comparison
In addition to the network, using the right data transfer tool is critical
Data transfer test from Berkeley, CA to Argonne, IL (near Chicago). RTT = 53 ms, network capacity = 10Gbps.
    Tool Throughput
    scp: 140 Mbps
    HPN patched scp: 1.2 Gbps
    ftp 1.4 Gbps
    GridFTP, 4 streams 5.4 Gbps
    GridFTP, 8 streams 6.6 Gbps
    Note that to get more than 1 Gbps (125 MB/s) disk to disk requires properly engineered storage (RAID, parallel filesystem, etc.)
© 2015, Energy Sciences Network
Notes: Comparison of legacy and recommended tools.
Note that rsync over HPN-SSH is reasonable in a 1Gbps environment – if you are stuck with rsync over SSH, at least use HPN-SSH.
Globus is now deployed at a large number of major scientific sites – the basic data transfer functionality is free.
=-=-=-
Parallelism is important
  It is often easier to achieve a given performance level with four parallel connections than one connection
  Several tools offer parallel transfers, including Globus/GridFTP
Latency interaction is critical
  Wide area data transfers have much higher latency than LAN transfers
  Many tools and protocols assume a LAN
Workflow integration is important
Key tools: Globus Online, HPN-SSH

## Slide 35: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2015, Energy Sciences Network

## Slide 36: Science DMZ Security
Goal – disentangle security policy and enforcement for science flows from security for business systems
Rationale
  Science data traffic is simple from a security perspective
  Narrow application set on Science DMZ
    Data transfer, data streaming packages
    No printers, document readers, web browsers, building control systems, financial databases, staff desktops, etc.
  Security controls that are typically implemented to protect business resources often cause performance problems
Separation allows each to be optimized
© 2015, Energy Sciences Network

## Slide 37: Performance Is A Core Requirement
Core information security principles
  Confidentiality, Integrity, Availability (CIA)
  Often, CIA and risk mitigation result in poor performance
In data-intensive science, performance is an additional core mission requirement: CIA  PICA
  CIA principles are important, but if performance is compromised the science mission fails
  Not about “how much” security you have, but how the security is implemented
  Need a way to appropriately secure systems without performance compromises
Collaboration Within The Organization
  All parties (users, operators, security, administration) needs to sign off up this idea – revolutionary vs. evolutionary change.
  Make sure everyone understands the ROI potential.
© 2015, Energy Sciences Network
Notes: You can still have really tight security if you need really tight security – just do it in a way that does not cause performance problems for traffic permitted by policy
Collaboration Within The Organization

## Slide 38: Security Without Firewalls
Data intensive science traffic interacts poorly with firewalls
Does this mean we ignore security? NO!
  We must protect our systems
  We just need to find a way to do security that does not prevent us from getting the science done
© 2015, Energy Sciences Network
Key point – security policies and mechanisms that protect the Science DMZ should be implemented so that they do not compromise performance
Traffic permitted by policy should not experience performance impact as a result of the application of policy

## Slide 39: Firewall Performance Example
Observed performance, via perfSONAR, through a firewall:
Observed performance, via perfSONAR, bypassing firewall:
Almost 20 times slower through the firewall
Huge improvement without the firewall
© 2015, Energy Sciences Network
Notes: Real life example, in front of and in back of a firewall that was dramatically impacting performance
perfSONAR is good at finding these issues
Engineers still have to take action to fix the problem

## Slide 40: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2015, Energy Sciences Network

## Slide 41: Challenges to Network Adoption
Causes of performance issues are complicated for users.
Lack of communication and collaboration between the CIO’s office and researchers on campus.
Lack of IT expertise within a science collaboration or experimental facility
User’s performance expectations are low (“The network is too slow”, “I tried it and it didn’t work”).
Cultural change is hard (“we’ve always shipped disks!”).
Scientists want to do science not IT support
The Capability Gap
© 2015, Energy Sciences Network
Notes: The struggle in engagement – management, engineering, and users often have dug in on bad behavior.
This amounts a capability gap – there is a disconnect from the capabilities of the network and the ability of the scientists to effectively use it
To fix this, we need to get everyone working toward a common goal:
- Management must fund and support the base needs of research
- IT is there to support the users in doing things correctly, and having all components work

## Slide 42: Bridging the Gap
Implementing technology is ‘easy’ in the grand scheme of assisting with science
Adoption of technology is different
  Does your cosmologist care what SDN is?
  Does your cosmologist want to get data from Chile each night so that they can start the next day without having to struggle with the tyranny of ineffective data movement strategies that involve airplanes and white/brown trucks?
© 2015, Energy Sciences Network

## Slide 43: The Golden Spike
We don’t want Scientists to have to build their own networks
Engineers don’t have to understand what a tokomak accomplishes
Meeting in the middle is the process of science engagement:
  Engineering staff learning enough about the process of science to be helpful in how to adopt technology
  Science staff having an open mind to better use what is out there
© 2015, Energy Sciences Network

## Slide 44: Establishing Requirements
http://www.es.net/about/science-requirements/network-requirements-reviews/
The purpose of these reviews is to accurately characterize the near-term, medium-term and long-term network requirements of the science conducted by each program office.
The reviews attempt to bring about a network-centric understanding of the science process used by the researchers and scientists, to derive network requirements.
We have found this to be an effective method for determining network requirements for ESnet's customer base.
© 2015, Energy Sciences Network
Notes: 2006
ELI + company
Led to science DMZ and other important end site innovations

## Slide 45: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
On the Topic of Security
User Engagement
Wrap Up
© 2015, Energy Sciences Network

## Slide 46: Why Build A Science DMZ Though?
What we know about scientific network use:
  Machine size decreasing, accuracy increasing
  HPC resources more widely available – and potentially distributed from where the scientists are
  WAN networking speeds now at 100G, MAN approaching, LAN as well
Value Proposition:
  If scientists can’t use the network to the fullest potential due to local policy constraints or bottlenecks – they will find a way to get their done outside of what is available.
Without a Science DMZ, this stuff is all hard
  “No one will use it”. Maybe today, what about tomorrow?
  “We don’t have these demands currently”. Next gen technology is always a day away

## Slide 47
The Science DMZ design pattern provides a flexible model for supporting high-performance data transfers and workflows
Key elements:
  Accommodation of TCP
    Sufficient bandwidth to avoid congestion
    Loss-free IP service
  Location – near the site perimeter if possible
  Test and measurement
  Dedicated systems
  Appropriate security
Support for advanced capabilities (e.g. SDN) is much easier with a Science DMZ
Wrapup
© 2015, Energy Sciences Network

## Slide 48: The Science DMZ in 1 Slide
Consists of four key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with end users
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
© 2015, Energy Sciences Network
Notes: Single slide summary

## Slide 49: Links
  ESnet fasterdata knowledge base
    http://fasterdata.es.net/
  Science DMZ paper
    http://www.es.net/assets/pubs_presos/sc13sciDMZ-final.pdf
  Science DMZ email list
    Send mail to sympa@lists.lbl.gov with the subject "subscribe esnet-sciencedmz”
  Fasterdata Events (Workshop, Webinar, etc. announcements)
    Send mail to sympa@lists.lbl.gov with the subject "subscribe esnet-fasterdata-events”
  perfSONAR
    http://fasterdata.es.net/performance-testing/perfsonar/
    http://www.perfsonar.net
© 2015, Energy Sciences Network

## Slide 50
  engage@es.net
  Ask us anything:
  Preparing for CC-DNI
  Deploying perfSONAR
  Debugging a problem
  Attending a training event
  Designing a network
© 2015, Energy Sciences Network

## Slide 51: Thanks!
Jason Zurawski – zurawski@es.net
Science Engagement Engineer, ESnet
Lawrence Berkeley National Laboratory
KINBER Webinar
March 4th 2015