## Slide 1: Use Cases
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
Jason Zurawski – zurawski@es.net
Kate Petersen – kate@es.net
RMACC Symposium and RMCMOA Workshop
August 11th 2016
http://www.es.net/science-engagement/science-requirements-reviews/
© 2016, The Regents of the University of California, through Lawrence Berkeley National Laboratory (subject to receipt of any required approvals from the U.S. Dept. of Energy). All rights reserved.
NOTICE. This material is owned by the U.S. Department of Energy. As such, the U.S. Government has been granted for itself and others acting on its behalf a paid-up, nonexclusive, irrevocable, worldwide license in the material to reproduce, prepare derivative works, and perform publicly and display publicly.

## Slide 2: Outline
Introduction
Examples
  ALS Workflow
  APS Science DMZ
Conclusions

## Slide 3: Introduction
Engagement with end users normally starts with a scripted set of things to address
  All items from case study template
  Info on traffic flow (if you have it)
  A previous complaint or request (if one was made)
The individual fixes from an engineering perspective can diverge into categories
  Host tuning/upgrades
  Introduction of new software
  Network tuning/upgrades
  Sociological factors (new approaches to known problems)
Here are a couple of quick examples and outcomes

## Slide 4: Outline
Introduction
Examples
  ALS Workflow
  APS Science DMZ
Conclusions

## Slide 5: Advanced Light Source

## Slide 6: Advanced Light Source

## Slide 7: Big Science Now Comes in Small Package
Notes:     Beamline 8.3.2 at the Advanced Light Source is a Synchrotron-based Hard X-ray Micro-Tomography instrument. It allows non-destructive 3-Dimensional imaging of solid objects at a resolution of approximately 1 micron.
    106 increase in data output compared to previous generation
    8 Gbps flows to supercomputer for real-time analysis

## Slide 8: Application – Capture to Results
Basic Energy Sciences (BES) supports fundamental research to understand, predict, and ultimately control matter and energy at the electronic, atomic, and molecular levels in order to provide the foundations for new energy technologies and to support DOE missions in energy, environment, and national security.
http://science.energy.gov/bes/

## Slide 9: E Pluribus Unum
After processing on a supercomputer, models are created.
Hundreds to thousands of images are created in a few hours…they can range in size from MB to TB
9 – ESnet Science Engagement (engage@es.net) - 9/15/16
Processing on this order of magnitude can’t be done locally – we need to send (over a network) to a more capable facility

## Slide 10: User Workflow: Beamline 8.3.2
Users
Publications
1. Allocation
2. Endstation
3. Sample
4. Control Software
5. Data Collection
6. Data Transfer / Management
7. Data Processing
9. Write and edit
8. Data Analysis / Info Extraction / Visualization / Simulation

## Slide 11
Science Workflow Consultation
Notes: X-ray tomography beamline
General purpose network
Windows shares on an old computer with not enough storage
Data acquisition uses LabView
Data written to shared drive on firewalled Windows server
Analysis done on workstations
  High-powered Windows hosts
  Mix of proprietary and open-source tools
  Scientists can be physically present or use Remote Desktop
Data export post-analysis – physical transport of portable media
  USB hard drives

## Slide 12: Improved Workflow Infrastructure
Notes: Dedicated infrastructure, built for performance, outside the general purpose network, clear path to NERSC
Data acquisition uses LabView
Data written to SAMBA share on beamline Linux DTN
  Writing via SAMBA is faster than local disk on acquisition computer
  Data are TIFF files ~10MB each, ~1000 files per data set
  Current max performance is ~200MB/sec
Automated workflow pushes data to NERSC for analysis
  Workflow managed using signal files
  Data set is rolled up into an HDF5 file
  Python scripts drive Globus Online CLI
  Data transferred to NERSC DTNs at ~300MB/sec
Analysis results pulled back to beamline DTN
  Additional analysis done on workstations (still use some proprietary tools)
  Primary data export is via Globus Online from beamline DTN

## Slide 13: One Beamline Data Flow Tripled Network Use for a DOE Supercomputing Center

## Slide 14: Outline
Introduction
Examples
  ALS Workflow
  APS Science DMZ
Conclusions

## Slide 15: APS Science DMZ
Building on the success of ALS, we approached the APS (Advanced Photon Source) at Argonne National Laboratory about a similar effort.
Goal(s):
  Establish a Science DMZ Network for a small number of beamlines
  Measurement before/after network performance
  Upgrade data movement hardware
  Measurement before/after data movement performance
  Onboard users to the system, and upgrade home institutions (as needed)

## Slide 16: GM/CA
General Medical Sciences and Cancer Institutes Structural Biology Facility @ APS
  Focused on the study of crystallographic structure determination of biological macromolecules by X-ray diffraction
Typical User:
  Visits and spends some allocated time with samples and the beamline machinery
  Mails samples, controls device remotely
  In either case – data has to go ‘somewhere’

## Slide 17: Current Design

## Slide 18: Current Design

## Slide 19: ANL Border to ESnet New York (perfSONAR Test)

## Slide 20: GM/CA to ESnet New York (perfSONAR Test)

## Slide 21: GM/CA to ANL Border (perfSONAR Test)

## Slide 22: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 23: Pilot Network
Plan:
  Use campus and building fiber resources for 2nd path
  Applies to only a limited set of resources (perfSONAR, DTN)
Benefits
  Bypass congested local infrastructure
  Apply targeted (vs. blanket) security policy
Cautions:
  Prevent just ‘anything’ from using fast path – policy to control this
  Still need to figure out cause of local issues (e.g. this isn’t a pave over)

## Slide 24: perfSONAR Results

## Slide 25: perfSONAR Results

## Slide 26: perfSONAR Results

## Slide 27: perfSONAR – what about GridFTP?
Setup of the DTN Architecture:
  2 Servers
  Shared filesystem
  Each server has 2 interfaces/routes:
    Science DMZ routes (plumbed to specific external locations via ANL, ESnet/MREN) and avoiding slower path
    Traditional routes over slower path
  Goal: show that with the correct network the *SAME* underlying infrastructure can perform as well as the perfSONAR testing

## Slide 28: Testing ESnet CERN (long RTT) to GMCA
Scale is Mbps
Across the board improvement of around 5x-20x
Exercise helped to tune filesystem performance.
Chart: 
| 10G (single file) | 50G (single file) | 100G (single file) | 500G (single file) | 50G (medium files & deep dirs) | 150G (medium files & shallow dirs) | 500G (large files)
GMCA idb DMZ | 987.654 | 1238.39 | 1362.862 | 1164.822 | 587.717 | 1265.823 | 944.241
GMCA idb | 289.855 | 263.505 | 264.201 | 290.255 | 118.871 | 180.234 | 45.793

## Slide 29: Testing GMCA to ESnet CERN (long RTT)
Metadata operations (e.g. deeply nested directories) coupled with smaller files remains hard to crank up
Chart: 
| 10G (single file) | 50G (single file) | 100G (single file) | 500G (single file) | 50G (medium files & deep dirs) | 150G (medium files & shallow dirs) | 500G (large files)
GMCA idb DMZ | 1142.857 | 1290.323 | 1353.638 | 1251.956 | 574.713 | 1229.508 | 2960.77
GMCA idb | 300.752 | 322.061 | 266.667 | 246.945 | 190.749 | 211.268 | 420.315

## Slide 30: Testing GMCA to ESnet LBL (medium RTT)
Metadata operations (e.g. deeply nested directories) coupled with smaller files remains hard to crank up
Chart: 
| 10G (single file) | 50G (single file) | 100G (single file) | 500G (single file) | 50G (medium files & deep dirs) | 150G (medium files & shallow dirs) | 500G (large files)
GMCA idb DMZ | 1000 | 1219.512 | 1228.879 | 1688.476 | 756.144 | 2127.66 | 3642.987
GMCA idb | 509.554 | 307.929 | 104.167 | 251.889 | 122.474 | 650.407 | 1117.006

## Slide 31: Future
Wider use @ APS
  Solution now goes directly to a specific beamline – how to support the entire facility?
Wider use @ ANL
  Service for other research groups (e.g. ALCF, ARM, etc.)
  Pool of DTN resources w/ Globus, instead of each group manning their own (allows to back up to communal storage)
Defining Policy
  ACLs – ports exposed for things like perfSONAR, Globus. Shut off for things that don’t need it. Gray area is defining what is and is not science.
  Who gets on, who doesn’t
  Managing routing @ the border to best utilize the available WAN links

## Slide 32: Outline
Introduction
Examples
  ALS Workflow
  APS Science DMZ
Conclusions

## Slide 33: Conclusion
Many scientific disciplines are moving toward a model that automates the process
  Upgraded networks
  Access to computation (somewhere)
  Advanced software
Adopting these superfacility workflows earlier will help convince those that do not have a good handle on technology to move in that direction
This simplifies the IT job – less special snowflakes

## Slide 34: Superfacility elements multiply with growing interconnectedness. 2025 DOE Light sources:
Detectors capable of generating terabit data streams.
Computational tools for analysis, data reduction, feature extraction in situ, using advanced algorithms and specialized hardware.
Increased scientific throughput from robotics and automation software.
Data management and sharing, with federated identity management and flexible access control.
Post-processing: reconstruction, inter-comparison, simulation, visualization.
Integration of experimental and computational facilities in real time, using programmable networks.

## Slide 35
Lightsource
Superfacility
Prototype
2015

## Slide 36: Use Cases
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
Jason Zurawski – zurawski@es.net
Kate Petersen – kate@es.net
RMACC Symposium and RMCMOA Workshop
August 11th 2016
http://www.es.net/science-engagement/science-requirements-reviews/
© 2016, The Regents of the University of California, through Lawrence Berkeley National Laboratory (subject to receipt of any required approvals from the U.S. Dept. of Energy). All rights reserved.
NOTICE. This material is owned by the U.S. Department of Energy. As such, the U.S. Government has been granted for itself and others acting on its behalf a paid-up, nonexclusive, irrevocable, worldwide license in the material to reproduce, prepare derivative works, and perform publicly and display publicly.

## Slide 37: Extra Slides